## Slide 1
MOTION PLANNING IN THE BROWSER
Can It
Fit?
Will the sofa make it through the hallway? Let's build the room, then let a robot-style planner figure it out — and learn how it thinks.
Notes: Hi Everyone, I'm Can! Have you ever been stuck on a staircase, holding one end of a couch, thinking: "there is no way this fits"?
Today we're going to settle that argument with math.
I built a browser app called Can It Fit, where you can design a room in 3D, drop in a piece of furniture, and a motion planner will figure out whether it can actually get through.
In the next few minutes I'll show you how to use it, and then, the fun part, how the planner really solve the problem. No installs. No build step. Just a browser.
Let's go.

## Slide 2
THE PROBLEM
Moving a couch is a 6-dimensional puzzle
It slides in 3 directions: x, y, z
It spins in 3 ways: yaw, pitch, roll
Walls, corners and doorways don't care how clever you are
"Does it fit?" really means: is there a collision-free path through 6-D space?
Notes: Here's why this is harder than it looks.
A couch isn't just sliding along a hallway. It can move in three directions, and it can rotate in three ways: yaw, pitch and roll. That's six degrees of freedom.
So "does it fit?" is secretly a question about finding a path through six-dimensional space, where every single pose along the way has to avoid every wall.
Look at this corner. The sofa can't just slide through. It has to turn, at exactly the right moment, by exactly the right amount.
That turning is what makes this problem interesting.

## Slide 3
WHAT YOU'LL SEE
One app, three ways to answer it
Probabilistic solver
RRT-Connect.
Deterministic solver
a deterministic straight-shot heuristic.
Manual mode
Hold M, drag the furniture yourself. The app tells you when you collide.
1 Build
2 Entrance & exit
3 Furniture
4 Solve
Notes: This app gives you three ways to answer the question.
First, manual mode, where you grab the furniture yourself and try it virtually.
Second, a deterministic straight-shot heuristic.
Third, a probabilistic solver using motion planning algorithm called RRT-Connect,
and Everything follows four simple steps: build the room, choose the entrance and exit, describe the furniture, and solve. Let's walk through each one.

## Slide 4
HANDS-ON · STEP 1
Build the room
Drag the A / B / C length sliders. Try 8 · 2.4 · 2.4 — instant hallway.
Change the angles to skew it, or hit the 45° two-face box template.
Need a turn? + Add object → Connect two objects → click a face on each.
Every room is a box: O + s·A + t·B + u·C, with s, t, u from 0 to 1. Turn on vector labels to see A, B, C.
Notes: Step one: build the room.
[DEMO: drag the A, B and C length sliders]
I'll set A to eight, and B and C to two point four. And just like that, we have a hallway.
Change the angles between the vectors and the box skews. There's even a one-click forty-five degree template.
Need a corner? Add a second object, hit "Connect two objects", and click a face on each. Now you have an L-shaped hallway.
Turn on the vector labels and you can see A, B and C right on the model.

## Slide 5
HANDS-ON · STEP 2
Choose the entrance & exit
Press Pick faces in 3D view.
Click an outside wall: first the entrance, then the exit. (Or use the dropdowns.)
Press Confirm 3D model — the room locks.
Only these two faces are doorways. Every other wall stays solid — the furniture can't cheat through them.
Notes: Step two: tell the planner where the furniture comes in, and where it has to come out.
Press "Pick faces in 3D view". Click an outside wall for the entrance, which turns green, then click another for the exit, which turns orange. You can also use the dropdowns.
Then press "Confirm 3D model", and the room locks.
Here's the key rule: these two faces are the only doorways. Every other wall is solid, so the furniture can't cheat.
And if you change your mind later, just click step one or step two in the progress bar and the room unlocks again.

## Slide 6
HANDS-ON · STEP 3
Describe the furniture
Enter Length · Width · Height. Try 2.5 · 1.2 · 1.2.
The green box is your furniture, parked beside the room. Show furniture in 3D view to focus it.
Set Clearance (0.1) — a safety margin around every side.
Furniture is one rigid box. Clearance grows the box in every direction before any collision check.
Notes: Step three: describe your furniture.
Enter the length, width and height. I'll use two point five by one point two by one point two.
That green box next to the room is your sofa.
Then set the clearance, which is a safety margin around every side. And here's the important detail: clearance doesn't just add a rule at the end. It actually inflates the box in every direction before any collision check.
So a clearance of point one means the planner treats your sofa as slightly fatter than it really is. That's realistic, and it's deliberately conservative.

## Slide 7
HANDS-ON · STEP 4A
Try it yourself first
Try manually — the furniture starts fully outside the entrance.
Hold M and drag. Use the sliders for height, yaw, pitch, roll.
Stuck at a corner? Auto Pilot: click a furniture edge, then a room edge — they snap parallel.
■ inside, legal ■ outside ■ collision
You win when the furniture passes completely through the exit — a pop-up tells you.
Notes: Before we let the computer try, try it yourself.
Press "Try manually". The furniture starts fully outside the entrance.
[DEMO: hold M and drag the furniture in]
Hold M and drag. Use the sliders for height, yaw, pitch and roll. Watch the colour: green means you're inside and legal, yellow means you're still outside, and red means you've collided with a wall.
Stuck at a corner? Try Auto Pilot. Click an edge of the furniture, then an edge of the room, and the app snaps them parallel for you.
Get all the way through the exit and you win.
I promise it's harder than it looks, and that's exactly why we need a planner.

## Slide 8
HANDS-ON · STEP 4B
Now let the solver try
Pick RRT-Connect or Heuristic, then Run selected solver.
A pop-up gives the verdict: It fits! or No route.
Scrub the timeline. Colours: green clear, yellow tight, red collision.
Failed? Raise max iterations, allow roll sampling, reshape the room — or go back a step.
Notes: Now let the planner try.
Choose RRT-Connect or Heuristic, and press "Run selected solver".
[DEMO: run it]
When it's done, a pop-up gives you the verdict: "It fits!", or "No route found". Close it, and scrub the timeline to watch the sofa travel through the room. Green means clear, yellow means tight, red means a collision.
If it fails, you have options. Raise the max iterations. Allow roll sampling. Reshape the room. Or just click back a step and change the furniture. Nothing is locked in.

## Slide 9
UNDER THE HOOD
How does it
actually work?
1 · Pose
How is a position stored?
2 · Collision
How do we know it's legal?
3 · Search
How do we find a path?
Notes: So far you've seen what it does. Now let's open the hood.
Three questions. How is a position stored? How do we know a position is legal? And how do we search for a path?
By answering those three questions, you will understand the whole planner.

## Slide 10
TECHNIQUE · 1
A position is six numbers
// furniture pose
{ x, y, z,
yaw, pitch, roll }
3 to translate, 3 to rotate
Rotations use Euler order ZYX, converted to a quaternion
Allow roll sampling off? The search drops to 5-D — faster
Notes: Question one: how do you describe where a couch is?
With six numbers. X, Y and Z for position, and yaw, pitch and roll for rotation.
The code stores that as a simple object, and converts the three angles into a quaternion, using Z-Y-X Euler order. We use the same convention everywhere, so rendering, collision checking and saving always agree.
And here's a neat trick: turn off "Allow roll sampling" and the search drops from six dimensions to five. That makes it faster, and most furniture never needs to barrel-roll anyway.

## Slide 11
TECHNIQUE · 2
Is this pose legal?
Every point must be inside the room
Between two poses we interpolate and check every step
Crossing a wall is allowed only through the entrance / exit polygon
Notes: Question two: given a pose, is it legal?
If every boundary point of the furniture is inside the room, the pose is legal.
To check a move between two poses, we interpolate and test every little step along the way.
And crossing a wall? That's only allowed through the entrance or exit.
It's the exact same check for manual mode and for both solvers. Nobody gets special treatment.

## Slide 12
TECHNIQUE · 3
RRT-Connect: two trees, one path
One tree grows from the start, one from the goal
Then the other tree greedily chases that new node
Trees touch → path found. Smooth it, resample it, animate it
Probabilistic: finding a route proves it fits — failing doesn't prove it can't. Run it again or raise iterations. We never "fix" failures by quietly shrinking clearance.
Notes: Question three: how do we find a path through six-dimensional space?
With an algorithm called RRT-Connect. RRT stands for Rapidly-exploring Random Tree.
Specifically, RRT-Connect grows two trees, one from the start and one from the goal.
It randomly samples new nodes in each iteration, attempting to connect the two trees while avoiding the obstacles.
When the two trees touch, we have a path. We smooth it, resample it, and animate it.
One honest caveat. It's probabilistic. So Finding a route proves the furniture fits.
But failing to find one does not prove it can't. You may try run it again, raise the iterations, or use the manual solver.

## Slide 13
TECHNIQUE · 4
Smart starts beat pure luck
Random sampling alone rarely threads a tight doorway. So we seed the search:
Sample offsets across the opening × 15° yaw / pitch / roll orientations
Refine the promising ones at 5°
Probe inward: how deep does each candidate get?
Rank by depth, clearance, alignment, offset, tilt
Feed the top poses as many starts and goals
Notes: Pure random sampling struggles with a tight doorway. The chance of randomly guessing a good entrance pose is tiny.
So we don't start blind. We sample offsets across the opening, combined with fifteen-degree yaw, pitch and roll orientations. We refine the promising ones at five degrees. Then we probe each candidate inward, to see how deep it gets.
We rank them by depth, clearance, alignment, offset and tilt, and feed the best ones to the planner as candidate starting poses.
And this will increase the chance of successfully finding a path.

## Slide 14
TECHNIQUE · 5
The straight-shot heuristic
Travel direction = the block edge not in the entrance face
Point the furniture's longest axis along it
Project the doorway along that direction: does the cross-section (with clearance) fit?
Centre it, stage it outside, slide straight in
Deterministic, instant, and when it fails it names the checkpoint where it got stuck. Multi-block rooms hand off between blocks with a short RRT.
 | RRT-Connect | Heuristic
Idea | Random search | Slide it in straight
Result | Different each run | Same every run
Handles turns | Yes | Via handoffs
On failure | Try again | Shows the stuck spot
Notes: The second solver is the straight-shot heuristic, and it's the opposite of random.
The travel direction is the room edge that isn't part of the entrance face. We line up the furniture's longest axis with it, project the doorway along that direction, and check whether the furniture's cross-section, with clearance, fits through.
If it does, we centre it, park it outside, and slide it straight in.
For rooms made of several blocks, it hands off between blocks using a short RRT.
My rule of thumb: use the heuristic for a fast yes on simple straight room, and RRT-Connect when you need real manoeuvring.

## Slide 15
YOUR TURN
Challenge: find the tipping point
Build an L-shaped hallway: two blocks (5 * 2 * 2), connected end to end
Furniture (1.5 * 1.2 * 1.2), clearance 0.1
Try it manually, then run both solvers
Increase the furniture size until it stops fitting
Does roll sampling rescue it?
🛋️
What's the largest sofa that fits your hallway?
Share your number in the comments.
entrance
exit
Notes: Now it's your turn.
Build an L-shaped hallway out of two connected blocks. You can make furniture and clearance of this size
Try it manually first. Then run both solvers.
Then increase the furniture size until it stops fitting, and see whether roll sampling rescues it.
So here's the question: what's the largest sofa that fits your hallway?
Pause the video, give it a go, and drop your number in the comments. I'm really curious what you find.

## Slide 16
TRY IT NOW
Open it in your browser
LAUNCH THE APP — NO INSTALL
volcano1998.github.io/FurnitureSim_3D
SLIDES + POWERPOINT
volcano1998.github.io/FurnitureSim_3D/slides
SOURCE CODE ON GITHUB
github.com/volcano1998/FurnitureSim_3D
Click any card to open it
Prefer to run it locally? One command: python3 -m http.server 8000 — see the README.
Thanks for watching — go move some couches.
Notes: That's everything. And the best part: you can try it right now.
The app is live in your browser. No install, no account. The link is on screen and in the description.
The full source code is on GitHub, so you can read the planner, change it, or even add your own solver.
Thanks so much for watching. Now go move some couches.